GPR Tracker
System Design
Draft 0.1
# Introduction
This document is about a planned GPR tracking and planning software and part of a contract between CatSurveys Ltd and the Department of Geodesy and Surveying of the Budapest University of Technology and Economics.
# Requirements
The scope given by CatSurveys. This section is the copy of the scope_for_software_development document-
Software description
We are looking to create a program which can help us position on site in real time, and track coverage with the GPR antenna. Desired, is the possibility of using for survey planning and the ability to apply this as a general software platform for all GPR users.
Main functions of the software
- Showing our position live, against a map background (Bing, google earth, etc.)
- Showing moving trajectory
  - This should be an arrow pointing in the direction the vehicle is moving, based on the trajectory of the last few points recorded. This could be an indication if we are moving off track.
- Adjustable coverage width, shown on screen. This would be due to antenna width selection
- Be able to create lines to follow on site, or load in from pre-planned data (CAD, kml etc.)
  - This function should be both with drawing lines on a map background, or by recording lines on site, by driving, and using those lines to create parallels.
- Warning if getting off track from planned lines or be able to track “parallels” from previous scans. Could include an audible warning as well as visual

Proposed phases of the program
- Live tracking with width of the antenna against a map background
- Drawing in or importing in lines
- Trajectory and guidance
# Software and hardware background
The target of the software development is a QGIS plug-in. A Python plug-in is planned to add the necessary functionality.
Our work is heavily based on available free software. Using free software rapid development can be achieved. There are many free software to display, handle and edit maps. QGIS is the market leader among these. It has many advantages:
- Full featured GIS software
- Platform independent (Windows, Linux and OSX)
- Extendable writing Python or C++ plug-ins
- Supports international standard

Any hardware which can run QGIS 3.x is usable. Probably laptops and Windows tablets are the best for the field work. Android will not be supported.
The GNSS (GPS) receiver must be able to send NMEA messages through a serial line (RS-232) or Bluetooth to the computer. For precise positioning an RTK ready GNSS receiver is necessary.
Internet connection is necessary on the field if on-line background map (e.g. Google Maps, Bing, OSM, etc) is used.
# Workflow
Data flow
GNSS
receiver
Serial line
Bluetooth
QGIS
Planned
route
Archive
track

The GNSS receiver is set to send GGA messages per second (or other reasonable time interval) to the computer through the serial line or Bluetooth connection. The plug-in adds the point to the archive track and refresh the track on the map, moves the map view if necessary to show the actual position near to the center of the view. If there is an active planned route the position is compared to the planned route.
# User interface
The user interface will be integrated into the QGIS GUI. Plug-in specific menu options, toolbar icons and dialog windows extend the base QGIS GUI using the Qt application framework.
Using the Parameter settings dialog the user can set the working environment. Available parameters are
- Tracking on/off
- GPR width
- Layer for active track (optional, if not set no track drawn, saved)
- Layer for active route (optional, if not set no route is checked)
- Alarm on/off (if there is an active route)
- Alarm distance, distance limit from the active route)
- GNSS connection settings (e.g. COM1, Bluetooth address)
- ...
# GNSS interface
This part of the plug-in will handle the input NMEA stream through the serial or Bluetooth interface. It is based on the standard pyserial and bluetooth Python modules.
New: virtual ports or port splitter https://freeserialportsplitter.com/
# Track logging
Points from the GNSS NMEA stream are added to the track log if logging is active. The track log is a four dimensional QGIS line layer, the fourth dimension is the time of the vertex (the fourth dimension is the so called M value (Unix time) in GIS). Tracks are saved to QGIS line layers (shape files, GeoPackage or other QGIS supported format). So tracks are routes can be analyzed later, too.
# Route planning
Before planning the user have to draw the polygon of the area of interest on a visible layer in QGIS using QGIS editing functionality. Considering the GPR width the planner creates a zigzag line parallel to the longest side of the given polygon. The user can change the direction of the zigzag lines. The planned route is saved to the hard disk, too. For grid scanning of an area two route plans have to be created in perpendicular directions.
# Track-route control
If the a route and the alarm are on the distance of the active position is calculated from the planned route. Not only the nearest point of the active route to the actual position have to be found, but track length should be also considered. If the distance from the route is over the limit alarm is sent to the user (beep or visual feed back).